## Slide 1: The water that makes the Barley
Advocating for less water and more beer.

## Slide 2: Crop change Barley
Based on reported water use (FAO) Barley requires half the irrigated water than Pistachios.
ET from Barley ( 0.003 mm/day) vs Pistachios (0.006 mm/day)
Required pumping for Barley is 2250 cubic meters per day vs 4500 for Pistachios
Plus, you can use it to make beer!

## Slide 3: Well Placement
Move the well closer to river, so it draws more from river than storage; reduces impact on Aquaseca's well
Agricultural field is nearby and down gradient, so less pipeline costs

## Slide 4
NEW WELL
OLD WELL

## Slide 6: Examples of Normalized Head Plots

## Slide 7: Changes in drawdown at Aquaseca well
Ensemble | Number | Initial Drawdown | Barley Drawdown | Well Move Drawdown | Both Drawdown
1333113 | 0 | -4.39 | -4.38 | -4.38 | -4.38
3133113 | 1 | -0.50 | -0.49 | -0.48 | -0.48
3111331 | 2 | -0.58 | -0.53 | -0.57 | -0.53
1111331 | 3 | -9.89 | -9.65 | -9.77 | -9.58
2121331 | 4 | -2.14 | -2.03 | -2.11 | -2.02
2121311 | 5 | -2.15 | -2.04 | -2.13 | -2.03
2122111 | 6 | -2.15 | -2.04 | -2.13 | -2.03
2213223 | 7 | -1.00 | -0.96 | -0.95 | -0.94
2211221 | 8 | -1.38 | -1.23 | -1.34 | -1.22
1111111 | 9 | -10.05 | -9.77 | -9.99 | -9.74
Notes: Arrows indicated min and max

## Slide 8: Drawdown as a percentage
Number | Barley difference (%) | Well move difference (%) | Both difference (%)
0 | 0.3 | 0.1 | 0.2
1 | 2.8 | 3.3 | 4.6
2 | 7.6 | 1.1 | 8.8
3 | 2.4 | 1.3 | 3.2
4 | 5.1 | 1.1 | 6.0
5 | 5.3 | 0.9 | 6.0
6 | 5.2 | 0.9 | 6.1
7 | 3.4 | 4.4 | 5.9
8 | 10.8 | 3.1 | 13.2
9 | 2.8 | 0.6 | 3.2
Average | 4.6 | 1.8 | 5.7
Notes: Arrows indicate min and max

## Slide 9
 | Storage Changes |  |  |  | 
 | Ensemble | Number | 100 Year Barley Crop change from Proposal | 100 year Well Move Change from Proposal | 100 year Well+Barley Change from Proposal
Min % Change | 1333113 | 0 | 36.2% | 39.9% | 57.1%
Min Head Change | 3133113 | 1 | 39.0% | 45.9% | 62.4%
Max % Change | 2211221 | 8 | 40.4% | 2.7% | 41.8%
Max Head Change | 1111111 | 9 | 39.1% | 5.1% | 41.1%

## Slide 10
 | Stream Leakage |  |  |  | 
 | Ensemble | Number | Barley vs Pistachio Difference | Well Move vs Proposal | Combined Diff from Proposal
Min % Change | 1333113 | 0 | -2.97% | 10.13% | -1.58%
Min Head Change | 3133113 | 1 | -3.91% | 0.28% | 0.99%
Max % Change | 2211221 | 8 | -2.12% | 0.31% | -1.94%
Max Head Change | 1111111 | 9 | -7.58% | 6.79% | -3.41%
 | Average Change: |  | -4.14% | 4.38% | -1.48%
Notes: Estimated errors for ensembles 0 and 1 are 5.5 to 6.5%
Estimated errors for ensmembles 8 and 9 are <0.5% and <0.05%

## Slide 11: Model performance
The damp
  Affected the quality of the solution
  Varied based on which parameter had high values in the ensemble
    Sensitive to K and Sy
Outputs every timestep
  Decreased efficiency
Ensemble | Number | Damp value
1333113 | 0 | 0.01
3133113 | 1 | 0.01
3111331 | 2 | 0.1
1111331 | 3 | 0.9
2121331 | 4 | 0.5
2121311 | 5 | 0.9
2122111 | 6 | 0.5
2213223 | 7 | 0.1
2211221 | 8 | 0.5
1111111 | 9 | 0.9

## Slide 12: Honorable Mentions
Alternative ag well placement
Pros:
  Less effect on town well
Cons:
  Cost of delivery
  Permitting
  Further from ag field
Conclusion – keep well on same side of river
Location of farm
Pros:
  Less effect on town’s well
Cons:
  GroMore complaints
  Aquaseca more concerned with the ag well
Conclusion – don’t move it
Notes: The location of the irrigation well. But, the ag interest will fight it if the well is farther from the farm than in the proposed plan. (They are concerned about permitting and cost of delivery.)
The crop. But, the ag interest will not be happy about being restricted to a potentially lower value crop.
The location of the farm. But, the ag interest has worked out a pretty good deal for the land, so they will resist this, too.
a summary of the alternate designs you considered and why you didn't select them

## Slide 13: Recommendations
Crop change and well move
  Less impact on Aquaseca well
  Water delivery cost decreases
  Future growth and increased pumping possible
  Beer